## Slide 1: MEETING_2&3_1FEB&15FEB
Nitin D. Patwari
Anjul Srivastavs

## Slide 2: Work progress
Sr. No. | Date | To Do | Done
1) | 1st JAN to 18th JAN | Go through the papers and decide the feasibility to implement them. | Studied both the papers and overviewed the basic concepts required to understand the paper. Decided to implement paper [1] then [2].
2) | 18th JAN to 1st Feb | Implement Karatsuba multiplier. | Implemented Conventional multiplier. Started implementation of Karatsuba multiplier (completed for operands of the form n=2m).
3) | 1st Feb to 15th Feb | Implement Karatsuba multiplier for n={93, 131, 163, 193, 233, 283, 409} | Done implementation of Karatsuba multiplier for n={93, 131, 163, 193, 233, 283, 409}
1] An Efficient and High Speed Overlap Free Karatsuba Based Finite Field Multiplier for FGPA Implementation.
2] Cryptographic Accelerators for Digital Signature Based on Ed25519.

## Slide 3
Sr. No. | Date | To Do | Done
4) | 15th FEB to 1st MAR | Implementation of OKA and OBS. | 

## Slide 4: Previous Meeting Questions
Explanation of Karatsuba Multiplier with an example.
How does the number of Xor gates in Karatsuba Multiplier and Overlap-free Karatsuba Multiplier same?
KA 4bit Multiplier
OKA 4bit Multiplier

## Slide 5: Conventional Multiplier
Conventional Multiplier (CM)
e.g.
Effective polynomial representation
e.g. 10100001=x7+x5+1.
AND gate
XOR gate

## Slide 6: Theoretical Area and Delay for CM
CAXOR(n) = (n − 1) 2
CAAND (n) = (n) 2
Number of Gates = CAXOR(n) + CAAND (n)
TCA(n) = Ta + log2(n) Tx
n | 2 | 4 | 8 | 16 | 32 | 64 | 93 | 163 | 193 | 233 | 283 | 409
No. of gates | 5 | 25 | 113 | 481 | 1985 | 8065 | 17113 | 52813 | 74113 | 108113 | 159613 | 333745
TCA (Tg) | 2 | 3 | 4 | 5 | 6 | 7 | 7.53916 | 8.34873 | 8.5925 | 8.8642 | 9.1447 | 9.67595

## Slide 7: Karatsuba Multiplier (KA)

## Slide 8: Karatsuba Multiplier (KA)

## Slide 9: Theoretical Area and Delay for KA
KAXOR(n) = 6 nlog2(3) − 8n + 2
KAAND(n) = nlog2(3)
Number of Gates = KAXOR(n) + KAAND (n)
TKA(n) = Ta + ( 3 log2(n) − 1)Tx .
n | 2 | 4 | 8 | 16 | 32 | 64 | 93 | 163 | 193 | 233 | 283 | 409
No. of gates | 7 | 33 | 127 | 441 | 1447 | 4593 | 8485 | 21154 | 27809 | 37699 | 51576 | 93242
TKA (Tg) | 3 | 6 | 9 | 12 | 15 | 18 | 19.6 | 22.046 | 22.777 | 23.593 | 24.434 | 26.0279

## Slide 10: Overlap Free Karatsuba (OKA)

## Slide 11: Overlap Free Karatsuba (OKA)

## Slide 12: Theoretical Area and Delay for OKA
KAXOR(n) = 6 nlog2(3) − 8n + 2
KAAND(n) = nlog2(3)
Number of Gates = KAXOR(n) + KAAND (n)
TKA(n) = Ta + ( 2 log2(n) − 1)Tx .
n | 2 | 4 | 8 | 16 | 32 | 64 | 93 | 163 | 193 | 233 | 283 | 409
No. of gates | 7 | 33 | 127 | 441 | 1447 | 4593 | 8485 | 21154 | 27809 | 37699 | 51576 | 93242
TKA (Tg) | 2 | 4 | 6 | 8 | 10 | 12 | 13.078 | 14.697 | 15.185 | 15.728 | 16.289 | 17.3519

## Slide 13: Plot: Number of gates

## Slide 14: Plot: Number of delay

## Slide 15: Implementation of CM
1) Wrote python program to generate Verilog code for implementation of n bit CM.
2) wrote test-bench
3) Compared the output with result of online calculator
(http://www.ee.unb.ca/cgi-bin/tervo/calc.pl)

## Slide 16: Implementation of KA for n=2m
1) Wrote python program to generate Verilog code for implementation of n=2m bit KA.
2) wrote test-bench
3) Compared the output with result of online calculator
(http://www.ee.unb.ca/cgi-bin/tervo/calc.pl)

## Slide 17: KA for 64 bit

## Slide 18: Work done between 1stFEB - 15thFEB

## Slide 19: How odd number multiplicand KA implemented !
n={93, 131, 163, 193, 233, 283, 409}

## Slide 20: KA for 233 bit

## Slide 21: THANK YOU !!